## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Boolean Algebra and Logic Simplification
© 2008 Pearson Education

## Slide 2: In this Chapter…
Objectives:
Laws and Rules of Boolean Algebra
Standard Forms of Boolean Expression
Simplification by using algebra rules
Karnaugh map and logic simplification

## Slide 3
In Boolean algebra, a variable is a symbol used to represent an action, a condition, or data. A single variable can only have a value of 1 or 0.
The complement represents the inverse of a variable and is indicated with an overbar. Thus, the complement of A is A.
Boolean variable
A literal is a variable or its complement.

## Slide 4
Boolean Addition
Addition is equivalent to the OR operation. The sum term is 1 if one or more if the literals are 1. The sum term is zero only if each literal is 0.
Example
Determine the values of A, B, and C that make the sum term of the expression A + B + C = 0?
Solution
Each literal must = 0; therefore A = 1, B = 0 and C = 1.

## Slide 5
In Boolean algebra, multiplication is equivalent to the AND operation. The product of literals forms a product term. The product term will be 1 only if all of the literals are 1.
Boolean Multiplication
Example
What are the values of the A, B and C if the product term of A.B.C = 1?
Solution
Each literal must = 1; therefore A = 1, B = 0 and C = 0.

## Slide 6
Commutative Laws (交换律)
In terms of the result, the order in which variables are ORed makes no difference.
The commutative laws are applied to addition and multiplication. For addition, the commutative law states
A + B = B + A
In terms of the result, the order in which variables are ANDed makes no difference.
For multiplication, the commutative law states
AB = BA

## Slide 7
Associative Laws (结合律)
When ORing more than two variables, the result is the same regardless of the grouping of the variables.
The associative laws are also applied to addition and multiplication. For addition, the associative law states
A + (B +C) = (A + B) + C
For multiplication, the associative law states
When ANDing more than two variables, the result is the same regardless of the grouping of the variables.
A(BC) = (AB)C

## Slide 8
Distributive Law (分配律）
The distributive law is the factoring law. A common variable can be factored from an expression just as in ordinary algebra. That is
AB + AC = A(B+ C)
The distributive law can be illustrated with equivalent circuits:
AB + AC
A(B+ C)

## Slide 9
Rules of Boolean Algebra
1. A + 0 = A
2. A + 1 = 1
3. A . 0 = 0
4. A . 1 = A
5. A + A = A
7. A . A = A
6. A + A = 1
8. A . A = 0
9. A = A
=
10. A + AB = A
12. (A + B)(A + C) = A + BC
11. A + AB = A + B

## Slide 16
Rules of Boolean Algebra
Rules of Boolean algebra can be illustrated with Venn diagrams (文氏图). The variable A is shown as an area.
The rule A + AB = A can be illustrated easily with a diagram. Add an overlapping area to represent the variable B.
The overlap region between A and B represents AB.
The diagram visually shows that A + AB = A. Other rules can be illustrated with the diagrams as well.
=

## Slide 17
A
Rules of Boolean Algebra
A + AB = A + B
This time, A is represented by the blue area and B again by the red circle.
The intersection represents AB.
Notice that A + AB = A + B
Example
Solution
Illustrate the rule with a Venn diagram.

## Slide 18
Rules of Boolean Algebra
Rule 12, which states that (A + B)(A + C) = A + BC, can be proven by applying earlier rules as follows:
(A + B)(A + C) = AA + AC + AB + BC
= A + AC + AB + BC
= A(1 + C + B) + BC
= A . 1 + BC
= A + BC
This rule is a little more complicated, but it can also be shown with a Venn diagram, as given on the following slide…

## Slide 19
The area representing A + B is shown in yellow.
The area representing A + C is shown in red.
Three areas represent the variables A, B, and C.
The overlap of red and yellow is shown in orange.
ORing with A gives the same area as before.
=
(A + B)(A + C)
A + BC
The overlapping area between B and C represents BC.

## Slide 20
Rules of Boolean Algebra

## Slide 21
DeMorgan’s Theorem (德·摩根定理)
The complement of a product of variables is equal to the sum of the complemented variables.
DeMorgan’s 1st Theorem
AB = A + B
Applying DeMorgan’s first theorem to gates:

## Slide 22
DeMorgan’s Theorem
DeMorgan’s 2nd Theorem
The complement of a sum of variables is equal to the product of the complemented variables.
A + B = A . B
Applying DeMorgan’s second theorem to gates:

## Slide 24
Apply DeMorgan’s theorem to remove the overbar covering both terms from the
expression X = C + D.
DeMorgan’s Theorem
Example
Solution
To apply DeMorgan’s theorem to the expression, you can break the overbar covering both terms and change the sign between the terms. This results in
X = C . D. Deleting the double bar gives X = C . D.
=

## Slide 28
Boolean Analysis of Logic Circuits
Combinational logic circuits can be analyzed by writing the expression for each gate and combining the expressions according to the rules for Boolean algebra.
Apply Boolean algebra to derive the expression for X.
Example
Solution
Write the expression for each gate:
Applying DeMorgan’s theorem and the distribution law:
C (A + B )
= C (A + B )+ D
(A + B )
X = C (A B) + D = A B C + D
X

## Slide 29
Boolean Analysis of Logic Circuits
Use Multisim to generate the truth table for the circuit in the previous example.
Example
Solution
Set up the circuit using the Logic Converter as shown. (Note that the logic converter has no “real-world” counterpart.)
Double-click the Logic Converter top open it. Then click on the conversion bar on the right side to see the truth table for the circuit (see next slide).

## Slide 30
Boolean Analysis of Logic Circuits
The simplified logic expression can be viewed by clicking
Simplified expression

## Slide 31: Logic Simplification
Why simplification?
  In software design, simpler logic means less program branches and simpler codes
  In hardware design, simpler logic means less gates, lower cost and less energy consumption
Ways to simplify logic functions
  With rules in Boolean Algebra
  With Karnaugh map

## Slide 32: Logic Simplification
  AB+A(B+C)+B(B+C)
  =AB+AB+AC+BB+BC
  =AB+AC+B+BC
  =B(A+1+C)+AC
  =B+AC
Solution
Example
Simplify the logic function below.
  AB+A(B+C)+B(B+C)

## Slide 33: Logic Simplification
AB+A(B+C)+B(B+C)=B+AC

## Slide 34: Logic Simplification
Solution
Example
Simplify the logic function below.